Instructions on how to ramp launch from your Special

Float-Off Triad Trailer.

1)  Back the trailer tires to the waters edge and chock the trailer tires with adequate wheel chocks.  This will prevent the trailer from rolling backwards.

2)  Using the front trailer jack, disconnect the trailer from the tow vehicle and move the tow vehicle forward enough to pull out the trailer extension bar.

3)  Prior to extending the extendable tongue pull the 5/8 inch release pin on the front airplane wheel and set the airplane wheel in the down position.  Reinsert the 5/8 inch hitch pin in the bottom of the airplane wheel arm

5/8 inch hitch pin

5/8 inch hitch pin

Airplane wheels in

Airplane wheels in stowed position                                     launching mode

Instructions continued on next page

4) Re-move the 5/8 inch hitch pin holding the extendable tongue in the stowed position.  Begin to slide the extendable tongue out towards the tow vehicle.  In the aft end of the extendable tongue there is a hole drilled which matches the hole in the extendable tongue collar.  When the extendable tongue is in the extended position, re-pin the extended tongue through the extendable tongue.  Caution!  The extendable tongue is very heavy therefore it is recommended that 2 people perform step 4.

Extendable tongue collar

5/8” hitch pin

Extendable tongue in stowed position

6) With the extendable tongue extended, re-couple the extension bar to the tow vehicle.  You are now ready to back the boat and trailer down the ramp.  IMPORTANT!  Before you back the trailer into the water make sure you retract the tongue jack.  You will not need the trailer jack to support the tongue weight of the trailer with the extension bar extended.  The front airplane wheels will carry all the tongue weight of the trailer.

7) Back the trailer up into the water and stop backing up when you feel the keel of the boat has lifted off the keel support.

8) Set the trailer winch in the reverse position and begin to let the boat out slowly.  Your winch may be equipped with a hand brake which can be used to control the speed that the boat floats off the trailer.  Please never take your hand off of the winch handle as it may spin out of control and cause injury.  Towards the end of this manual are the instructions on how to properly use your trailer winch.

9) To retrieve the boat reverse the directions listed above.