Maintenance Schedule for Triad Trailers equipped with

Electrically activated hydraulic drum brakes

All tasks in highlighted cells must be performed as indicated intervals

| Item | Function Required | Weekly | 3 Months or 3000 Miles | 6 Months or 6000 Miles | 12 Months or 12000 Miles |
| --- | --- | --- | --- | --- | --- |
| Brakes | Test that they are operational. | At Every Use |
| Brake Adjustment | Adjust to proper operating clearance. |  |  |  |  |
| Brake Magnets | Inspect for wear or current draw. |  |  |  |  |
| Brake Linings | Inspect for wear or contamination. |  |  |  |  |
| Brake Controller | Check for correct amperage & modulation. |  |  |  |  |
| Brake Cylinders | Check for leaks, sticking. |  |  |  |  |
| Brake Lines | Inspect for cracks, leaks, kinks. |  |  |  |  |
| Trailer Brake Wiring | Inspect wiring for bare spots, fray, etc. |  |  |  |  |
| Breakaway System | Check battery charge and switch operation. | At Every Use |
| Hub/Drum | Inspect for abnormal wear or scoring. |  |  |  |  |
| Wheel Bearings & Cups | Inspect for corrosion or wear. Clean & repack. |  |  |  |  |
| Seals | Inspect for leakage. Replace if removed. |  |  |  |  |
| Springs | Inspect for wear, loss of arch. |  |  |  |  |
| Suspension Parts | Inspect for bending, loose fasteners, wear. |  |  |  |  |
| Hangers | Inspect Welds. |  |  |  |  |
| Wheel Nuts and Bolts | Tighten to specified torque values. |  |  |  |  |
| Wheels | Inspect for cracks, dents or distortion. |  |  |  |  |
| Tire Inflation Pressure | Inflate tires to mfg's specifications. |  |  |  |  |
| Tire Condition | Inspect for cuts, wear, bulging, etc. |  |  |  |  |