Instructions on how to ramp launch 
from your Float-Off Triad Trailer.

1)  Back the trailer tires to the waters edge and chock the trailer tires with adequate wheel chocks.  This will prevent the trailer from rolling away while you prepare to ramp launch.

2)  Utilizing the front trailer jack, disconnect the trailer from the tow vehicle and move the tow vehicle forward enough to pull out the trailer extendable tongue.

3) Re move the two 1/2 inch or 5/8 inch trailer hitch pins shown below.

1/2 inch or 5/8 inch pins

4) Begin to slide the extendable tongue out towards the tow vehicle.  Located at the aft end of the extendable tongue are two holes drilled which match the holes in the extendable tongue collar.  When the extendable tongue is in the extended position, re-pin the extended tongue through the extendable tongue collar.

5) Now, re couple the extension bar back to the tow vehicle.  IMPORTANT!  Before you back the trailer into the water make sure you retract the tongue jack.  You will not need the trailer jack to support the tongue weight of the trailer with the extension bar extended.

6) Back the trailer up into the water and stop backing up when you feel the keel of the boat has lifted off the keel support.

7) Set the trailer winch in the reverse position and begin to let the boat out slowly.  Your winch may be equipped with a hand brake which can be used to control the speed that the boat floats off the trailer.  Please never take your hand off of the winch handle as it may spin out of control and cause injury.  Towards the end of this manual are the instructions on how to properly use your trailer winch.

8) To retrieve the boat reverse the directions listed above.