Instructions on how to ramp launch your

Float-Off Triad Trailer.

1)  Back the trailer tires to the waters edge and chock the trailer tires with adequate wheel chocks.  This will prevent the trailer from rolling away while you prepare to ramp launch.

2)  Utilizing the front trailer jack, disconnect the trailer from the tow vehicle and move the tow vehicle far enough forward to pull out the extendable tongue.

3)  Prior to pulling out the extendable tongue the brake system needs to be disconnected.  Locate the hydraulic surge brake disconnect which is located on the front drivers side of the trailer.  As shown below, pull the disconnect collar towards the back of the trailer and disengage the brake line.

5) Re move the two 1/2 inch or 5/8 inch trailer hitch pins shown below.

4) Begin to slide the extendable tongue out towards the tow vehicle.  Located at the aft end of the extendable tongue are two drilled holes which match the holes in the extendable tongue collar.  When the extendable tongue is in the extended position, re-pin the extended tongue through the extendable tongue collar.

5) Now, re couple the extension bar back to the tow vehicle.  IMPORTANT!  Before you back the trailer into the water make sure you retract the tongue jack.  You will not need the trailer jack to support the tongue weight of the trailer with the extension bar extended.

6) Back the trailer up into the water and stop backing up when you feel the keel of the boat has lifted off the keel support.

7) Set the trailer winch in the reverse position and begin to let the boat out slowly.  Your winch may be equipped with a hand brake which can be used to control the speed that the boat floats off the trailer.  Please never take your hand off of the winch handle as it may spin out of control and cause injury.  Towards the end of this manual are the instructions on how to properly use your trailer winch and trailer jack so the above steps can be performed safely.

8) To retrieve the boat reverse the directions listed above.

# Text boxes

Pull disconnect collar

towards back of trailer

Hydraulic surge brake disconnect collar shown in disengaged position

Hydraulic surge brake disconnect shown in engaged position

1/2 inch or 5/8 inch hitch pins